HellasGA Fly In – Ikaros field

The “See-and-Avoid, Safety First, Get-Together Fly-In”!

30 Sept. 2007

SAFETY BRIEFING

Please read through the following safety & operational instructions regarding the aircraft & pilots participating in this Fly In.

INBOUND flights

- Follow LGTG APP 120,250 or ATH Info. 130,925 instructions until reaching IKAROS area. Call Ikaros Air Ground Radio (A/G) 119,700 as early as possible

- The Fly In’s traffic circuit is at 1,300 ft AMSL with Tanagra QNH, always South of the airfield

- DO NOT descend below 2,300 ft AMSL unless you have established radio contact with Ikaros A/G

- Airport is licensed but (ATC) uncontrolled and therefore you must still check visually windsocks, runway etc. before landing. We suggest you plan to join overhead at 2~3,000 ft and follow A/G radio (119,700) suggestions.

- Most probably runway in use will be 27

- Even if you have good information by A/G, still keep a GOOD LOOK OUT for other traffic. CHECK FINAL approach before joining it from base leg.

GROUND

- Upon landing keep a good look out for pedestrians, young kids etc. The Fly In will have people on the ground to assist crowd control but still aircraft will need extra caution due to the congested space

- For the event there will be an operations frequency (Ops) on 123,400 that most probably you will be asked to contact as soon as you vacate the runway. Talk to OP’s 123,400 for any questions etc. and leave the A/G frequency free of unnecessary chatter

- Most probably, after vacating runway, you will be marshaled to park at the EAST GRASS area south of the runway marked with orange cones. Follow the marshaler’s suggestions but with caution, airport is uncontrolled

- Remember to CLOSE your FLIGHT PLAN with LGTG TWR 22620 45656 / 45685 / 45663. Ikaros has no direct contact with ATC authorities.

- Please remember to secure your aircraft in the parking position and remove the keys from the aircraft if unattended.

LOCAL FLIGHTS

- For local / pleasure flights please check in at the airport building’s office. Someone will be taking care of the schedule of aircraft and people who are interested to fly locally

- During local flights, if the airport pattern is congested, please avoid it and fly few miles to the West / Northwest for safety. Maintain 3,000 ft (AMSL) or above.

- For airport low passes inform A/G radio accordingly so that they inform other traffic in the circuit. Do not execute low passes outside the runway area (safety zone). Aerial displays are not on the scope of this Fly In.

- Keep a good look out for traffic in the circuit (South & 1,300 AMSL) and listen to A/G 119,700 suggestions. Check thoroughly the final approach area before entering the runway.

- Plan not to fly between 12:00 & 13:30L since an open discussion has been scheduled in the event. Plan your local flights between 13:30 & 16:00L according to event’s schedule.

- Remember, Megara LGMG closes at 18:00L and Tatoi LGTT at 18:50L

OUTBOUND

- Submit your FLIGHT PLANs at Athens Central Reporting Office 210 3533691. If unable, then call LGTG TWR (see above)

- First call Ikaros Op’s on 123,40 for start up and keep a GOOD LOOK out for CLEAR PROP before start up and during taxi operations

- Expect taxi suggestions by Op’s and to be asked to contact A/G 119,700 when reaching the runway holding point ready for departure but well CLEAR of the runway

- If proceeding to hold short at the East grass taxi link to runway 27 pay attention to the perimeter fence which is very close to the taxiway

- Check thoroughly the final approach area before entering the runway.

- On crosswind leg keep a good look out for aircraft entering downwind and climb to a minimum of 2,000ft

- Remember you are inside Tanagra MTMA and 120,250 should be contacted after leaving the Fly In area and before or upon reaching 2000ft AMSL

GENERAL

- Ikaros is licensed but officially an uncontrolled airfield. SEE & AVOID is your sole responsibility. Please listen and adhere to A/G suggestions & information to maximize safety.

- The Fly In will have lots of pedestrians and young kids wandering around the airport grounds. Although Ikaros will do their best to keep them away from moving aircraft & live propellers, please do your best as well to keep a good look out.

- In the traffic circuit if there is more than one aircraft airborne try to maintain the standard circuit lateral & vertical pattern and a speed of 80kts~90kts

- Please keep transmissions as short and accurate as possible as it could get pretty busy at peak traffic hours.

- Please use landing LIGHTS in the Fly In area at any time until runway is vacated. Use taxi lights, rotating beacons & strobes as appropriate in the air & on the ground to warn of approaching aircraft and/or propeller about to go live.

- Please be precise in your position and time estimate reports so as to facilitate A/G radio in suggesting some safe & efficient traffic separation.

- Half a mile east of the airport there is a r/c models strip. The Fly In team will ask the operators to keep well clear of Ikaros traffic.

- Two miles to the North, KOPAIDA grass strip is operational. Keep a good look out and avoid flying too far north of Ikaros if below 2,300 ft

- If you need any help, call Op’s on 123,400 or Ikaros caretaker on 6932 418071

We wish you a safe and happy Fly In.

Ikaros & the HellasGA team